## Slide 1: Service Orchestration in Arrowhead -- G3.2 and beyond –
Csaba Hegedűs (hegeduscs@aitia.ai)
Pál Varga
AITIA Inc.
Budapest University of Technology

## Slide 2: Agenda
What is it designed for?
  Requirements and scenarios
  Principles
G3.2 orchestration
  Intra-Cloud orchestration fundamentals
  Inter-Cloud orchestration concepts, philosophy
  Inter-Cloud core architecture
Future work
  Where to next?
  Optimization of the framework

## Slide 3: Orchestration in various domains - RECAP
 | Orchestration | Security | Protocol stack | Implementations
Web Services | - orchestration: service composition at provider side - choreography: macro-lensed configuration of components for a specific target | - SSL/TLS using X.509 hierarchy - advanced authorization based on roles | -transfer: HTTP -data representation: mainly XML | - Java EE - Microsoft .NET Framework - DWPS
IT Clouds | - configuring cloud resources for service deployment - monitoring of deployment (telemetry) - event and error handling - policy-based orch. | - orchestrators configure security measurements - VPN solutions - Virtual Network Functions run by physical devices | - various, some based on e.g. HTTP | - IBM SmartCloud Orchestrator - Intel Ciao - Apex Lake
Software Defined Networking | - coordinate network resources and actives for new services - deployment of network virtual functions - deployment monitoring (QoS) |  | -various - OpenFlow - OpenStack | 
Formalized orchestration languages | - process control-flow description and verification | Not involved | - scripting languages (e.g. Java-based) | - Chor - ChorEvolution
Notes: Also:
We have to differentiate between private data and that of public interest.
We have to protect the systems that provide such data approprietly.

## Slide 4: Useful concepts here and there and their possible limits
 | Useful concepts | Inadequacies
Web Services | - applicable protocol stack - orchestration and choreography solutions | - large protocol stack overhead - only HTTP and XML - no real-time QoS capabilities
IT Clouds | - architecture for central governance of deployments - reconfiguration methodologies - performance monitoring, event detection techniques (telemetry) | - Instrumentational toolsets are connected to cloud and network resources - Requires advanced end-point capabilities - suited for infrastructure management
Software Defined Networking |  | 
Formalized orchestration languages | -scripting languages - evaluation methodologies | Mainly proof-of-concept

## Slide 5: Our definition of Orchestration
Primary high level target:
  Tell App. Systems what Services to consume and from where
  There shoud be both:
    on demand (upon request)
    a central push (initiated by central governance):
Secondary, implied targets:
  General management/ governance of the Local Cloud
    Provide reconfigurability of the SoS for operators
    Manage resources, their utilization (network and hardware QoS)
  There should be a layer for process engineers to plan their operations and enforce that new working order on the CPS-s.
  Arrowhead meta-layer: protocol independency
    Also provide translation if possible/necessary

## Slide 6: App. System autonomy levels
We should be able to facilitate App. Systems of increasing intelligence and self awareness.
They should be able to co-exist in an LC.
Passive Service Providers
  Only offer certain Services in limited number of interfaces.
  Only have to register in the SR
  Only have to respond to inbound connections, with proper AAA (preferably pre-rendered)
  Its resouces might have to be managed centrally (QoS: e.g. # of paralell inbound connections)
Statically pre-configured Service Consumers
  The App. System only consumes a pre-defined (hardwired) set of Services
  There might be multiple configuration modes (sleep, active, etc.)
  There is a list of hardwired Service Providers it is supposed to consume from
  Only needs the Orchestration Store

## Slide 7: App. System autonomy levels II.
3. Service Consumers with statically configured Service Providers
  Same as (2), but each Service might have backup Providers defined
  The Orchestrator might be asked to locate an available Provider based on a pre-set priority list stored in the Orch. Store
  Controllers can only access a specific temperature sensor, but there might be backups for that sensor
4. Fully autonomous Service Consumers
  System knows what Services and when it wants to consume.
  Orchestrator’s task is to locate appropriate Provider with selection criteria submitted by the requester Consumer
  E.g. electromobility use case in Arrowhead
5. Self-orchestrating Systems
  Implement all Core Service interfaces (SR, Auth, GK, QoS Mgr) and capable of running self-orchestration, choice between possible Service Providers
  Central management of resources and AAA might be still required.
  High level functioning systems

## Slide 8: App. System autonomy levels III.
6. System-of-Systems Configurators, Choreographers, Plant Description Engine
  Via HMI: human operators
  Capable of configuring the SoS, through the Core Framework
  Process engineering tools (similar to LabView or Matlab Simulink?)
  Should utilize „push” Orchestration/Reconfiguration capability through the Core Systems to enforce the new working order
  Further develop the Plant Description (see later)

## Slide 9: App. System security levels
No security
Resource constrained AA (~ticketing)
Certificates, without transactional authorization
Certificate with authorization tokens
App. Systems with built in authorization (self admission control)
We need handovers and interoperability between these different types.

## Slide 10: Deployment environments of the Framework
Based on the known (project) use cases: (sketch)
Production floor scenarios (factory automation)
  Real-time QoS, etc.
Across the production chain
  Multiple vendors, systems are advanced (ERP, data center, etc.)
  AAA is essential, and should be centralized inbetween companies
Market-like scenarios
  Virtual market of energy; electromobility
  App. Systems enter and leave; servicing is transactional/one-time only
  Offered and looked up Services vary over time
  The Orchestrator has to provide advanced matchmaking based on a multitude of metadata
Big data, cloud processing, CPS-s, WSN-s, etc.
  Like the MANTIS project
  Processing entity in the cloud; sensing, actuating, storing locally
  Company policies, use case dependent architecture: local and global clouds cooperating

## Slide 11: Therefore… (requirements engineering)
The Orchestration Service has to be:
Modular and its sub-processes optional for most part
  It should be tailorable by the LC developer/operator (via the Orch. Store)
  It should be tailorable by the Consumer (I am looking for a …)
Should have a simple interface (request-response)
  Unified data structures, one message body
  Request: small mandatory part, but custumizable
  Should try to be protocol independent
There might be:
  Hardwired connections (Orchestration Store)
  Ad hoc, dynamically orchestrated Services
We need an architecture that allows for centralized and decentralized governance of an LC

## Slide 12: G3.2 orchestration features and concepts

## Slide 13: G3.2 Core Framework
Minimum working set
Advanced working set (G3.2 and beyond)
Notes: Introduction and goals of AH
Local Clouds work in SOA.
There are the mandatory core systems, that offer basic governance.
Authorization now bears two tasks: access control information, token gen.
SR: now capable of cleaning up the database, implements service metadata with every offering separately.
Gatekeeper has two services: GSD, ICN.
Network Manager will be required to build up inter-cloud data end-to-end path.

## Slide 14: The current G3.2 Orchestrator (Milestone 2)
Used terminology: intra- and inter-Cloud orchestration
Consists of two modules:
  Orchestration Store (private, inner interface)
  Matchmaker logic (public)
Offers one public Service:
  Orchestration Service (not Orchestration Store Service)
Request-response based (currently JSON)
  Service Request Form
  Orchestration Response (List<OrchestrationForm>)
Capable of 3 orchestration types within one Service:
  Default configuration (for booting of App. Systems)
  Store-based orchestration (with a backup list of Providers for a given Service for a given Consumer)
  Dynamical orchestration
In the latter two, inter-Cloud orchestration is included if necessary

## Slide 15: Orchestration Service

## Slide 16: Reminder of the common descriptors within G3.2

## Slide 17: Service Request Form
Identity of the Consumer, mandatory
Requested Service (optional)
QoS, demonstration only
Preferences of the Consumer (dynamical orch.)
Flags that can be set by the Consumer to configure the Orch. Process
All of them are optional, by default False.

## Slide 18: Orchestration Response
The Response entity contains multiple Orchestrations.
The to-be-consumed Service (up to IDD)
The Provider’s identity (IP:port/baseURL)
The URL of the Service (after baseURL)
Token and signature (optional)
Special field that can pass extra configuration data serialized.
Currently only used by the „Default Config”.

## Slide 19: Default configuration (boot time)
For App. System initialization
Static, Orchestration Store entry
Service Request: minimal
  If SSL is used, could be reduced to a GET (not implemented)
Orchestration Response
  There can be additional configuration information passed („Instructions”)
  An ordered list of <Provider, Service, Instruction>
Intention:
  Firstly, you shall consume the „System Configuration Service” from SysConfig Store
  Secondly, consume the „ServiceDiscovery Service” from SR to register yourself
  Thirdly, consume again the „Orchestration” with a runtime request (passed in the Instruciton field)
Notes: A legalapvetőbb orchesztrációs módszer a legbutább rendszereknek az, hogyha felébrednek és megkérdezik mit kell csinálni.
Itt gondolhatunk arra, hogy az ábrán mutatott
Attól függően, hogy milyen képességekkel rendelkeznek az alkalmazási rendszerek (szenzorok  okos eszközökig), különféle orchesztrálási módszereket kell alkalmaznunk. Azonban ezeket egy szolgáltatásba összegyúrva, ??.

## Slide 20: Store-based Orchestration (runtime)
For runtime. There are hardwired connections with possible backup Providers.
The Orchestrator will return the highest priority one that is:
  online (PingProviders), currently authorized, satisfies QoS, etc.
For runtime; with integrated exception handling: re-orchestration (pull)
Dynamical and inter-Cloud orchestration is embedded within this type of Store entry, if necessary
Notes: It is good for creating backups, if a SP dies or not available anymore. Increases robustness.

## Slide 21: Dynamical orchestration
Finding an appropriate Provider (intra- or inter-Cloud) based on:
  Service and its metadata (from SRF)
  Preferences of the Consumer (from SRF)
  Requested QoS (from SRF)
  Currently available Providers and neighborhood Clouds

## Slide 22: Flags, flags, flags…

## Slide 23: Orchestration Store
Default config?
For maintenance.
Instruction for Consumer.
Priority of entry (Store-based)
Consumer ID
To-be consumed Service and Service Provider (and its Cloud);

## Slide 24: Token in the local orchestration process

## Slide 26: Intra-Cloud conclusions
The Orchestrator’s internal working can be tailored.
  By the developer (open sourceness)
  By the operator (Orchestration Store)
  By the App. Systems (OrchestrationFlags)
  The MATCHMAKING algorithm can also be customized (i.e. dedicated functions within the code)
Can utilize other Core Systems (but not mandatory!)
AAA is/can be embedded (e.g. no SSL with SSLwith token)
  All based on Service metadata
Can support multitude of App. System intelligence
  Dumb devices
  Smart devices
  Decentralized operations
Can be interface backwards compatible (TODO)
  With a limited functionality, and based on the implemented implicite DNS naming convention:
  sysName_sysGroup._afh-serviceName_serviceGroup_inteface._tcp.cloudName.operator.arrowhead.eu

## Slide 27: Inter-Cloud servicing architecture

## Slide 28: Inter-Cloud servicing
Fundaments:
  Local Clouds are autonomous and independent from each another
  Within an LC ther can be decentralized governance (minimal Core System functionality) or strict centralization -- from the outside, we don’t care!
  But inter-Cloud requires that there are central entities responsible:
    security: admission control (letting in external Systems) and AAA!
    creation of the data path inbetween Clouds: Gateway, Firewall exception
    App. Systems should not be bothered with every inter-Cloud request
  Therefore:
    During inter-Cloud orchestration, the 2 sets of Core Systems are negotiating.
    It is completely transparent for App. Systems
  Technical analogy: roaming in telecommunication

## Slide 29: The Gatekeeper Services
Global Service Discovery
Initiated by the Orchestrator of the original LC
To locate Clouds where the service is currently available for us
Inter-Cloud Negotations
Preparing the servicing and negotiating the terms

## Slide 30: Inter-Cloud orchestration process (from the inside)

## Slide 32: Inter-Cloud authorization
The Authorization System has a list which other LC is authorized to use which service from our LC.
  AuthorizationControl service extended
This can be further developed.
  Currently static rules.
  Should rely on corporate contracts.
ArrowheadCloud
ArrowheadService

## Slide 33: Arrowhead Inter-Cloud architectures
How to realize the Global Service Discovery functionality?
Which (other) Local Clouds do we ask when GSD?
How do we know them („discover the neighborhood”)?
We proposed three architectures:
  Completely closed Arrowhead Neighborhoods
    (Production plants)
  Peer-to-peer ad hoc detection of other Local Clouds
    (moving cars along the road, looking up local infrastructure)
  A cloud-of-clouds entity handling the interactions between Local Clouds
    (integration along the supply chain)
    (supply and demand)

## Slide 34: Closed Neighborhoods

## Slide 35: Cloud-of-Clouds

## Slide 36: Data path realizations between Clouds
To be release in G3.2 Milestone 3
Utilizes RabbitMQ (AMQP) broker between the gateways
TCP tunneling service between Consumer and Provider
  The Gateway is configured by its own Gatekeeper at the end of the inter-Cloud Negotiations process.

## Slide 37: Inter-Cloud orchestration with the token
Orchestrator
Gatekeeper
Gatekeeper
Orchestrator
Authorization
A
B
1
2
3
4
5
Gateway
Gateway
Consumer
Service Provider
7
7
8
9
10
10
10
9

## Slide 38: Benefits of this solution
Governance
  Intra-Cloud: centralized or decentralized
  Inter-Cloud: negotiations between the two Core System sets
Simple Orchestration Service definition
  Minimum payload: requester System identification (GET method)
  Maximum payload: Consumer preferences, detailed Flags, RequestedQoS, etc.
  Protocol independency (should work with MOM-s, e.g. MQTT/AMQP)
Built in multi-level AAA support
Possibility to re-configure SoS
  Process engineering
  Future work possibility
Builds on the use case defined level of interactions between Core entities
  Orchestration is customizable
  Can still utilize Orchestration Store, etc.
  General guidelines and maximum capability scenario is described here

## Slide 39: Future work

## Slide 40: Push Orchestration
Utilize the Event Handler, notify every App. System to re-request Orchestration
  SOS_CONFIG_CHANGE::ALL_SYSTEMS or ::”SYSTEM_GROUP_NAME” (e.g. only Systems on Production Line #1)
No need to implement Orchestration Push Service, just Event Handler subscribe
SoS_Config_Chg::ProdLine1

## Slide 41: Engineering tools to configure LC / SoS
SoS Configurator entity:
  Engineering tool
  Utilizes Plant Description, standardized process engineering
  Output writes into the core Stores
    Orchestration Store
    Authorization Store
    Gatekeeper settings
  Triggers re-orchestration of the SoS
    Or parts of the SoS
See article:
Oscar Carlsson, Csaba Hegedűs, Jerker Delsing, Pál Varga: Organizing IoT Systems-of-Systems from Standardized Engineering Data. In Proceedings of IECON 2016, Florence Italy, Oct. 2016.

## Slide 42: Engineering results in new SoS configuration
Plant Description
- functional layout of plant
Processes and systems
„what does what and how”
How the plant, processes and devices are mapped into Arrowhead Systems and Services
Production/Operation Plan
Operational targets (e.g. 452 cars)
Timeliness and process flows (chassis production then paint it, then…)
„what should do what and how”
Derived from business targets
Process engineering tools
Service Inventory
Process Flow
Breakdown of the work for Systems
Tasks, quantities, timeliness
Arrowhead
SoS Choreographer
Push configuration
Trigger re-orchestration
Device Registry

## Slide 43: Shortcomings / future work
  G3.2 implements all of this already
    Token generation is integrated in the released version (requires some work)
    Event Handler integration is not done
    Service Registry Bridge documentation and code cleanup is required (evopro)
  Gateway module is conceptual only (TODO)
    Should have an interface towards firewall/VPN/Phyiscal relay/etc.
    Should be application protocol independent
    Should be capable of handling the authorization token
  Interoperability between different LC-s and developer groups
    A simple DNS-SD naming convention is not enough for inter-Cloud service identification (hence the new Common Descriptor objects)
    Arrowhead Service Inventory (need something similar to WS UDDI)
      Smarter Service search (e.g. based on detailed descriptions, metadata, etc.)

## Slide 44: Shortcomings / future work II.
  Authorization System should rely on standards
    E.g. RADIUS AAA for access rights tables
    Token generation: e.g. OAuth, etc. (having resource constrained in mind)
    Handovers and interoperability between different security levels (e.g. if Provider is certificate based, while Consumer is very dumb sensor)
    Transaction/servicing level decentralized AAA: blockchains maybe (in one use case)
  Process engineering toolset, UI, integration into the Core Framework
    Continuation of the plant description work

## Slide 45: Requirements engineering concepts for Productive4.0 (SKETCHES)

## Slide 46: Deployment environments of the Framework
Based on the known (project) use cases: (sketch)
Production floor scenarios (factory automation)
  Real-time QoS, etc.
Across the production chain
  Multiple vendors, systems are advanced (ERP, data center, etc.)
  AAA is essential, and should be centralized inbetween companies
Market-like scenarios
  Virtual market of energy; electromobility
  App. Systems enter and leave; servicing is transactional/one-time only
  Offered and looked up Services vary over time
  The Orchestrator has to provide advanced matchmaking based on a multitude of metadata
Big data, cloud processing, CPS-s, WSN-s, etc.
  Like the MANTIS project
  Processing entity in the cloud; sensing, actuating, storing locally
  Company policies, use case dependent architecture: local and global clouds cooperating

## Slide 47: Clusterization of use cases
Dimensions:
Application System maturity, autonomy (1-6)
  Embedded systems  Fully fledged, no constraints
  computation, communication, energy constraints
Local Cloud security expectations (1-5)
  No security Transactional, per servicing level security
Servicing QoS and resource management
  Are there real time requirements?
  Is there QoS requirement towards the framework?
Data and control handling
  Use case specific requirements
  Mostly desired, key features of the frameworks
Digital production
Value chain integration
Logistics

## Slide 48: Optimizing for various use cases
Application System capability
Security, AAA
Resource and network QoS management
Data and control handling
X
X
X
X
X: use cases cluster #1
X: use cases cluster#2
X
X
X
X

## Slide 49: Optimized versions for various use cases
 | Embedded, streamlined, automation | Fully fledged, value chain integration | Publish-Subscribe, big data
Major target domains | Industrial automation, IIoT, edge processing | Product lifecycle management, supply chain integration, | Big Data collection and processing frameworks, IoT, edge to cloud interfaces
Key features | Streamlined, Store orchestration, event handling, fallback to backup Service Providers, push orchestration, engineering tools, | Scalability of the Core Systems, dynamical and inter-Cloud orchestration, App. System preferences, AAA, logging, web of trust, smart service contracts/ service metadata, protocoltranslation | Lookup, bootstrap, Service Provider metadata, scalability,
Protocols | - CoAP, minimalistic REST, binary UDP, … (SOA request-response) | REST, WS | OPC-UA, MQTT, AMQP, XMPP
To be deployed on | - Edge gateways, smart routers, … - ARM cores with lightweight Linux kernels (Raspberry Pi, OpenWrt) | Cloud infrastructure (private or public) VM servers | On the broker PC Edge gateways, local deployments
Development | One lightweight executable with all mandatory (&support) Core interfaces Modularly compilable („configurable make”, plugins) - C, C++ (Qt) | Java EE, servlet containers System image is needed (iso) | -
Clients | Microcontrollers, sensor motes, actuators, legacy devices with adapters Autonomy level <=3 | Autonomous Application Systems ERP, … Autonomy level > = 3 | Batch and stream processors, distributed databses in the cloud sensor motes, edge gateways
Security levels | intra-Cloud: rarely, primarily a closed network With secure, controlled outgoing link (inter-Cloud) Security level <=3 | Very high expected Blockchains, web of trust solutions should be researched Authorization Store rules should come from contracts, injection of rules with tools | - AAA of the MoM should be extended
Core interfaces | minimalistic, lightweight, maybe binary Should utilize the same protocol as app. services | More complex, flexible, Human readable and debuggable | Depending on target use case Should augment MoM capabilities

## Slide 50: Questionnaire for Prod4 WP1 partners
https://goo.gl/forms/C4tZK8ubJYEHHObG2

## Slide 51: ?
Thank you!

## Slide 52: Extending the QoS to service contracts
Network QoS | Core oversight QoS | Application service contract | Service Provider QoS
Latency (E2E) | Orchestration timeout |  | 
Packet loss | Re-orchestation required? |  |